## Slide 1
Major objectives of the largest proton-proton collider in the world, the Large Hadron Collider (LHC) at CERN, include the search for the Higgs Boson and Dark Matter.
In 2024, the LHC is set to be upgraded to the High-Luminosity LHC (HL-LHC), where the energy and rate of collisions will increase.
ATLAS, one of the four experiments, must replace its radiation-damaged detector with a new design that can withstand the higher luminosity.
Introduction
Context and Objectives
Variables:
Independent
  Template Length
  Minimum Match Score (MMS)
  Rotation Angle Range (RAR)
Dependent
  Resolution – Standard Deviation
  Accuracy – Mean
  Time to Pattern Match
VisuallyInspectPositions.vi was used to take 25 pictures of each corner. Using these pictures, templates of varying lengths and constant width were cut for Fiducial Marks F, E, I, and G (refer to the sensor diagram).
PatternMatch.vi was used to pattern match each of the four Fiducial Marks in each picture. This was repeated for each template, and for a second sensor.
Methods
Conclusions
The efficiency and accuracy of the pattern matching largely depends on the settings and the template. For each Fiducial Mark, there is a set up that optimizes pattern matching.
These findings are ultimately a small part of the whole. A majority of this project consists of developing the software and procedures for these tests. Since pattern matching is used throughout the assembly process, these procedures can be re-used. This will become a part of the stave assemble process, which will be used in the ATLAS experiment in the HL-LHC.
References
Acknowledgements and Contact Information
iriawang@brandeis.edu
The innermost part of the ATLAS detector is the inner tracker (ITk). It is made up of concentric cylinders, with a barrel and two end-caps.
A stave is a basic unit of the barrel. Each one has a stave core and 14 silicon sensors glued to each side.
Due to the precision of the science, each sensor must be within 25 micrometers of the ideal. To accomplish this, Fiducial Marks are used at each corner of the sensor.
Pattern matching in the programming language LabVIEW is used to identify the position of these marks, among other measurements, and thus must be tested for precision, accuracy, and efficiency.
Department of Physics, Brandeis University; Brookhaven National Laboratory
Iria Wang, Gabriella Sciolla
Optimizing Pattern Matching on Silicon Sensors for the Assembly of the ATLAS Experiment ITk Detector
Results
MMS Test: A low MMS increased the likelihood to pattern match incorrectly. A high MMS increased the likelihood of not finding a match. 800 MMS is ideal.
RAR Test: Using this function with any angle range takes 4x longer than turning this function off. Instead, the template should be cut to match the angle of the image.
Template Width: Template should just encompass the width of the Fiducial Mark.
Template Length: For each Fiducial Mark, there is an optimal range based on the efficiency (see table).
  Efficiency is defined as the fraction of pattern matches that are within 2 micrometers of the expected, and take less than 60 milliseconds to pattern match.
These test were carried out on a second sensor, yielding the same or similar results.
 | Mark F | Mark E | Mark I | Mark G
Min. Ideal length | 68x34 pixels | 62x32 pixels | 88x24 pixels | 74x26 pixels
Max. Ideal length | 68x50 pixels | 62x44 pixels | 88x36 pixels | 74x42 pixels
Ideal Templates

## Slide 2
Major objectives of the largest proton-proton collider in the world, the Large Hadron Collider (LHC) at CERN, include the search for the Higgs Boson and Dark Matter.
In 2024, the LHC is set to be upgraded to the High-Luminosity LHC (HL-LHC), where the energy and rate of collisions will increase.
ATLAS, one of the four experiments, must replace its radiation-damaged detector with a new design that can withstand the higher luminosity.
Introduction
Context and Objectives
Variables:
Independent
  Template Length
  Minimum Match Score (MMS)
  Rotation Angle Range (RAR)
Dependent
  Resolution – Standard Deviation
  Accuracy – Mean
  Time to Pattern Match
VisuallyInspectPositions.vi was used to take 25 pictures of each corner. Using these pictures, templates of varying lengths and constant width were cut for Fiducial Marks F, E, I, and G (refer to the sensor diagram).
PatternMatch.vi was used to pattern match each of the four Fiducial Marks in each picture. This was repeated for each template, and for a second sensor.
Methods
Conclusions
The efficiency and accuracy of the pattern matching largely depends on the settings and the template. For each Fiducial Mark, there is a set up that optimizes pattern matching.
These findings are ultimately a small part of the whole. A majority of this project consists of developing the software and procedures for these tests. Since pattern matching is used throughout the assembly process, these procedures can be re-used. This will become a part of the stave assemble process, which will be used in the ATLAS experiment in the HL-LHC.
Acknowledgements
Email: iriawang@brandeis.edu
The innermost part of the ATLAS detector is the inner tracker (ITk). It is made up of concentric cylinders, with a barrel and two end-caps.
A stave is a basic unit of the barrel. Each one consists of a long, flat, rectangular stave core with 14 modules glued to each side. Each module is an independent unit made of a silicon sensor and their read-out electronics.
Department of Physics, Brandeis University; Brookhaven National Laboratory
Iria Wang, Gabriella Sciolla
Optimizing Pattern Matching on Silicon Sensors for the Assembly of the ATLAS Experiment ITk Detector
Results
MMS Test: A low MMS increased the likelihood to pattern match incorrectly. A high MMS increased the likelihood of not finding a match. 800 MMS is ideal.
RAR Test: Using this function with any angle range takes 4x longer than turning this function off. Instead, the template should be cut to match the angle of the image.
Template Width: Template should just encompass the width of the Fiducial Mark.
Template Length: For each Fiducial Mark, there is a range for the ideal length based on the efficiency (see table).
These test were carried out on a second sensor, yielding the same or similar results.
 | Mark F | Mark E | Mark I | Mark G
Min. Ideal length | 68x34 pixels | 62x32 pixels | 88x24 pixels | 74x26 pixels
Max. Ideal length | 68x50 pixels | 62x44 pixels | 88x36 pixels | 74x42 pixels
Ideal Templates
Contact Information
This work was supported by Provost’s Undergraduate Research Fund. Thank you to Professor Gabriella Sciolla and the other students in the Sciolla Group who advised me throughout this project.
Analysis of Mark F and Mark E
Figure 1: An overhead view of the LHC and the four experiments around it.
Figure 2: A schematic of the ATLAS detector.
Figure 3: A candidate event display for the production of a Higgs boson decaying into two b-quarks.
Due to the precision of the science, each sensor must be within 25 micrometers of the ideal. To accomplish this, Fiducial Marks are used at each corner of the sensor.
Pattern matching in the programming language LabVIEW is used to identify the position of these marks, among other measurements, and thus must be tested for precision, accuracy, and efficiency.
Figure 4: A diagram of the new silicon sensor, ATLAS17LS, from the Technical Specification of ATLAS17LS Silicon Microstrip Sensor, Version 1.4.
Figure 5: The XYZ stage at the assembly station at Brookhaven.
Figure 6: The Front Panel of VisuallyInspectPositions.vi.
Figure 7: The Front Panel of PatternMatch.vi
Figure 8: Graphs analyzing Marks F and E.
Efficiency is defines as the fraction of patter matches that are within 2 micrometers of the expected, and take less than 60 milliseconds to pattern match
Figure 9: Templates of maximum and minimum ideal lengths for each Fiducial mark.