## Slide 1: Pattern Match Study: Abbreviated Results
Iria Wang

## Slide 2: Variables
Independent Variables
Template Length
Minimum Match Score (MMS)
Rotation Angle Range (RAR)
Dependent Variables
Resolution
  Standard deviation
Accuracy
  Mean
Time

## Slide 3: General Results
MMS: 800
  <800: usable, but likely to pattern match incorrectly
  >800: usable, but likely not to pattern match
RAR: none
  Takes 4x longer to pattern match
Template width: template should just encompass whole Fiducial Mark
Template length: there is an optimal range for each Fiducial Mark to minimize time and maximize accuracy
Studies were replicated on a second sensor with similar or the same results

## Slide 4: Mark F
Efficiency:
  Time: <60 ms to pattern match
  Accuracy: <2 um within expected
Optimal length: between 34 and 50 pixels
68x34
68x50

## Slide 5: Mark E
Efficiency:
  Time: <60 ms to pattern match
  Accuracy: <2 um within expected
Optimal length: between 32 and 44 pixels
62x44
62x32

## Slide 6: Mark I
Efficiency:
  Time: <55 ms to pattern match
  Accuracy: <2 um within expected
Optimal length: between 24 and 36 pixels
88x24
88x36

## Slide 7: Mark G
Efficiency:
  Time: <50 ms to pattern match
  Accuracy: <2 um within expected
Optimal length: between 26 and 42 pixels
74x26
74x42

## Slide 8: Problem…
Used optimal sizes to measure Fiducial to Fiducial – the skew is still there!!

## Slide 9: Problem…
Used optimal sizes to measure Fiducial to Fiducial – the skew is still there!!